Research talk 101
SciFi Mapping
John Williamson
University of Glasgow
November 2018

---
Purpose of a research talk
Overview
- Testing of mapping from optical fibres to Fadc channels for SciFi
- Plotting to confirm extraction of x and y co-ordinates from detector

---
SciFi overview
SciFi detector used for optics calibration: consists of 32 vertical and 32 horizontal fibers which can be used to obtain position of e beam
Each fiber read out into optical fibre then by PMT and ultimately Fadc250
Need for each channel of Fadc to be correctly calibrated and to make sure mapping (between channels and fibers) is correct

---
Map from fibres to optical guide

---
Map from fibres to optical guide
Maps for channels to optical guides tested using laser
Found that for both SciFi units that channels 9 & 11 were swapped with respect to previous diagram

---
Map from fibres to PMT
fibres
PMT

---
Map from fibres to PMT
fibres
PMT

---
Map from fibres to PMT

---
Stability of pedestals
Are these pedestals stable over time within a run and between runs?

---
Stability of pedestals
Between runs:

---
Stability of pedestals
Within runs:

---
Channel mapping
- Determining if pixel
  to Fadc map (and optical
  fiber to pixel map) is
  correct
- Needed for x-y (co-ord)
  information

---
Channel mapping
- Determining if pixel
  to Fadc map (and optical
  fiber to pixel map) is
  correct
- Needed for x-y (co-ord)
  information

---
Channel mapping
- Use scripts to plot x & y coords using existing maps (plots with source collimated in x-direction)

---
Channel mapping
- Now setting up second detector for testing testing
- Also creating analyzer class for SciFi such that it can process Fadc output in raw mode (for testing) or pulse mode for experiment

---
Experiment webpage
- Discussed last week
- Will be based on tritium webpage
- https://hallaweb.jlab.org/experiment/APEX/